## Slide 1: Real-Time Scheduling Simulator
Server-Based Algorithms for Mixed Periodic-Aperiodic Workloads
Shahab Afshar
CPR E 458/558: Real-Time Systems, Fall 2025
Department of Electrical and Computer Engineering
Instructor: Dr. G. Manimaran

## Slide 2: Problem Statement
Real-time systems must satisfy timing constraints in addition to functional correctness.
Real-World Example: Automotive Engine Control Unit (ECU)
An ECU must handle both predictable and unpredictable workloads:
  Periodic tasks: Engine control (10ms), ABS monitoring (5ms), fuel injection (20ms)
  Aperiodic tasks: Driver button presses, diagnostic requests, error handling
  Challenge: How to guarantee BOTH periodic AND aperiodic tasks meet deadlines?
The Gap in Current Tools
  Theoretical analysis provides utilization bounds but doesn't show temporal behavior
  Manual schedule construction is tedious and error-prone
  RTOS testing requires significant development effort before exploring alternatives
  Engineers need to explore algorithm behavior BEFORE committing to implementation

## Slide 3: Research Questions
This project investigates three research questions:
RQ1: Faithful Implementation
  Can a discrete-event simulator faithfully implement server capacity management policies (Polling, Deferrable, Sporadic)?
RQ2: Visualization Effectiveness
  Does interactive visualization (Gantt charts, metrics) help users understand algorithm differences?
RQ3: Parameter Exploration
  Can parameter exploration (varying server capacity Cs and period Ps) reveal optimal configurations?

## Slide 4: Solution: Four Server-Based Scheduling Algorithms
Server-based scheduling dedicates CPU capacity to aperiodic tasks while protecting periodic task deadlines:
Polling Server
  Capacity is LOST if no aperiodic tasks are ready when server executes. Simple but wasteful.
Deferrable Server
  Capacity is PRESERVED until end of server period. Better response but affects periodic schedulability.
Sporadic Server
  Capacity replenishment scheduled at t+Ps after consumption. Best response while maintaining RMS guarantees.
Background Scheduler
  Aperiodic tasks run ONLY during CPU idle time. Simplest but worst response time.

## Slide 5: Interactive Simulation Platform
A web-based simulator built with Python and Streamlit providing:
Core Features
  Discrete-event simulation with exact algorithm implementation
  Interactive Gantt charts showing task execution and server events
  Real-time parameter exploration via sliders (Cs, Ps, task parameters)
  21 preset configurations for quick experimentation
  Schedulability analysis with RMS, EDF, and DMS utilization bounds
Supported Algorithms
  Basic: RMS, EDF, DMS, LLF (Liu & Layland, 1973)
  Server-Based: Polling, Deferrable, Sporadic, Background
  Advanced: Precedence-constrained, Overload handling, HVDF

## Slide 6: Software Architecture
Layered Design with Clear Separation of Concerns
The architecture separates the simulation engine from visualization and UI, enabling independent testing and extension.
Technology Stack
Core Logic (Python 3.10+)
  Pure simulation engine with no UI dependencies. Implements all scheduling algorithms and produces ScheduleResult objects.
Visualization (Plotly)
  Creates interactive Gantt charts, priority timelines, and metrics dashboards from ScheduleResult data.
Web UI (Streamlit)
  Provides the interactive dashboard with configuration panels, result displays, and export functionality.
Data Handling (Pandas)
  Manages task tables, CSV/JSON export, and data transformation for visualization.

## Slide 7: Design Pattern: Template Method
Key Insight
All schedulers share the same simulation loop (time advancement, ready queue management, preemption handling). Only priority assignment and task selection differ.
Implementation
SchedulerBase implements the complete simulate() method. Subclasses override only two methods:
  assign_priorities(): How to assign priorities to tasks
  get_next_task(ready_queue): Which task to run next
Server Capacity Management
The key difference between servers is what happens when the server has CPU priority but no aperiodic tasks are ready:
  Polling: server_remaining = 0 (capacity lost)
  Deferrable: return False (capacity preserved until period end)
  Sporadic: Schedule replenishment at current_time + Ps

## Slide 8: Results: Correctness Validation (RQ1)
Can the simulator faithfully implement server capacity management?
Verification Method
Each server type produces characteristic events in the timeline. Correctness is verified by observing expected event patterns:
Polling Server: [Correct]
  capacity_lost events appear when server executes with no aperiodic tasks ready
Deferrable Server: [Correct]
  deferred events show capacity preservation; no capacity_lost events
Sporadic Server: [Correct]
  replenish events scheduled exactly at consumption_time + Ps
Background Scheduler: [Correct]
  Aperiodic execution only during idle intervals (no periodic tasks ready)
Answer: YES - The simulator correctly implements all four server algorithms as verified by behavioral event analysis.

## Slide 9: Results: Visualization Effectiveness (RQ2)
Does interactive visualization help users understand algorithm differences?
Visualization Features Implemented
Color-coded task bars
  Periodic tasks (blue), Aperiodic tasks (orange), Server capacity (green) are visually distinct
Deadline markers
  Red triangles mark absolute deadlines for each task instance
Arrival markers
  Green circles indicate task arrival times
Server event labels
  Events like 'replenish', 'deferred', 'capacity_lost' labeled directly on timeline
Hover tooltips
  Hovering over any bar shows task ID, remaining computation time, and event details
Interactive zoom/pan
  Users can zoom into specific time regions for detailed analysis
Answer: YES - Users can visually compare when capacity is lost (Polling) vs. preserved (Deferrable) vs. replenished (Sporadic).

## Slide 10: Results: Parameter Sensitivity (RQ3)
Can parameter exploration reveal optimal configurations?
Experiment Setup
Workload: Two periodic tasks P1(C=1, P=10), P2(C=1, P=15) and one aperiodic task A1(C=8, arrives at t=0). Server period Ps=5 fixed, varying capacity Cs.
Results: Server Capacity Effect on Response Time
Cs=2: Response Time = 17 time units (4 replenishment cycles needed)
Cs=4: Response Time = 9 time units (2 replenishment cycles needed)
Cs=8: Response Time = 8 time units (1 replenishment cycle needed)
Key Finding
Increasing server capacity (Cs) from 2 to 8 reduces aperiodic response time by 53% (17→8). This insight cannot be obtained from utilization formulas alone.
Answer: YES - Parameter exploration via sliders enables rapid discovery of optimal server configurations.

## Slide 11: Conclusions
Research Question Answers
RQ1: Faithful Implementation
  The simulator correctly implements capacity management for all four server algorithms, verified by observing expected event patterns (capacity_lost, deferred, replenish).
RQ2: Visualization Effectiveness
  Interactive Gantt charts clearly show when capacity is lost vs. preserved vs. replenished. Users can visually compare algorithm behavior side-by-side.
RQ3: Parameter Exploration
  Varying server capacity Cs from 2→8 demonstrated response time reduction from 178 time units, enabling discovery of optimal configurations.
Key Contributions
Open-source simulator implementing 4 server-based algorithms
Interactive Gantt charts displaying capacity management events
21 preset configurations from course literature for verified correctness
Parameter exploration via sliders for optimal configuration discovery
Schedulability analysis with RMS, EDF, and DMS utilization bounds

## Slide 12: Limitations & Future Work
Current Limitations
Single-processor only
  The simulator currently supports uniprocessor scheduling. Multi-core scenarios with task migration and partitioning are not yet implemented.
No resource contention modeling
  Priority Inheritance Protocol (PIP) and Priority Ceiling Protocol (PCP) are implemented in the codebase but not yet integrated into the main simulation loop.
Limited user validation
  RQ2 assessment is based on feature implementation. A formal user study would provide stronger evidence of visualization effectiveness.
Simplified execution model
  The simulator does not model I/O delays, cache effects, interrupt latency, or context switch overhead beyond basic counting.
Future Directions
Multi-core extension with partitioned and global scheduling algorithms
Resource protocol integration (PIP/PCP) for shared resource scenarios
RTOS trace import to compare simulation with FreeRTOS/Zephyr execution
Formal verification using model checking for schedulability guarantees

## Slide 13: Learning Achieved
Technical Skills Developed
Real-Time Systems Concepts
  Deep understanding of server-based scheduling (Polling, Deferrable, Sporadic), RMS utilization bounds n(2^(1/n)-1), schedulability analysis, and capacity management trade-offs.
Software Engineering Patterns
  Applied Template Method pattern for extensible scheduler architecture, Strategy pattern for composable priority policies, and event-driven simulation design.
Tools & Technologies
  Python for discrete-event simulation, Streamlit for rapid web UI development, Plotly for interactive visualizations, Pandas for data handling.
Key Lessons Learned
Simulation reveals temporal behavior that utilization formulas cannot show
Visualization is essential for understanding scheduling dynamics
Parameter exploration enables informed design decisions before implementation
Modular architecture (Template Method) dramatically simplifies adding new algorithms

## Slide 14: References
[1] B. Sprunt, L. Sha, and J. Lehoczky, "Aperiodic task scheduling for hard-real-time systems," Real-Time Systems, vol. 1, no. 1, pp. 27-60, 1989.
[2] J. P. Lehoczky, L. Sha, and J. K. Strosnider, "Enhanced aperiodic responsiveness in hard real-time environments," in Proc. IEEE Real-Time Systems Symposium, pp. 261-270, 1987.
[3] M. Spuri and G. Buttazzo, "Scheduling aperiodic tasks in dynamic priority systems," Real-Time Systems, vol. 10, no. 2, pp. 179-210, 1996.
[4] C. L. Liu and J. W. Layland, "Scheduling algorithms for multiprogramming in a hard-real-time environment," Journal of the ACM, vol. 20, no. 1, pp. 46-61, 1973.

## Slide 15: Thank You
Shahab Afshar
PhD Student, Computer Engineering
Department of Electrical and Computer Engineering
Project Repository: Available upon request